## Slide 1: I/O Virtualization
Hwanju Kim

## Slide 2: I/O Virtualization
Two ways of I/O virtualization
  I/O virtualization in VMM
    Rewritten Device drivers in VMM
    + High performance
    - High engineering cost
    - Low fault tolerance (driver bugs)
  Hosted I/O virtualization
    Existing device drivers in a host OS
    + Low engineering cost
    + High fault tolerance
    - Performance overheads
VMM
Guest VM
Block
device driver
Network
device driver
HW
Block device
Network device
Guest VM
VMM
Privileged VM
or Host OS
Block
device driver
HW
Block device
Block device
Guest VM
Network
device driver
Guest VM
Most VMMs (except VMware ESX Server) adopt
hosted I/O virtualization

## Slide 3: I/O Virtualization
I/O virtualization-friendly architecture
  I/O operations are all privileged and trapped
    Programmed I/O (PIO), memory-mapped I/O (MMIO), direct memory access (DMA)
  Naturally full-virtualizable
    “Trap-and-emulate”
    Issues
      1. How to emulate various I/O devices
        Providing a VM with well-known devices (e.g., RTL8139, AC97) as virtual devices
        Existing I/O device emulators (e.g., QEMU) handle the emulation of well-known devices
      2. Performance overheads
        Reducing trap-and-emulate cost with para-virtualization and HW support

## Slide 4: Full-virtualization
Trap-and-emulate
  Trap  hypervisor  I/O emulator (e.g., QEMU)
  Every I/O operation generates trap and emulation
    Poor performance
  Example: KVM
Guest VM
Guest OS
Host OS
(Linux)
KVM (kernel module)
QEMU
vCPU
vCPU
User space
Kernel space
I/O emulation
I/O operation
MMIO or PIO
Trap
Native drivers
Interrupt

## Slide 5: Para-virtualization
Split driver model
  Front-end driver in a guest VM
    Virtual driver to forward an I/O request to its back-end driver
  Back-end driver in a host OS
    Request a forwarded I/O to HW via native driver
Guest VM
Guest OS
Host OS
(Linux)
KVM (kernel module)
QEMU
vCPU
vCPU
User space
Kernel space
VirtIO
Backend
I/O operation
Native drivers
VirtIO
Frontend
Shared descriptor ring: Optimization by batching I/O requests
Reducing VMM
intervention cost

## Slide 6: Para-virtualization
How to reduce I/O data copy cost
  Sharing I/O data buffer (DMA target/source memory)
    A native driver conducts DMA to guest VM’s memory
    For disk I/O and network packet transmission
DomainU(id=1)
Domain0(id=0)
Xen
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 1 | 2 | 3 | 4
0 | 1 | 2 | 3 | 4
0 | 
1 | 
2 | 
3 | 
Native
Device driver
READ Sec 7
to PFN 3
0 | 
1 | 
2 | 
3 | 
Dom=0
MFN=6
Flag=R
Sec = 7
Dom = 1
REQ = R
GR = 1
Backend
driver
Foreign Map
to PFN 2
for WRITE
with GR 1
Dom=0
MFN=6
Flag=R
Disk
DMA READ
request
Unmap
Response
Grant table
Active
Grant table
Physical frame number (PFN)
Machine frame number (PFN)
Xen grant table mechanism

## Slide 7: Para-virtualization
How about network packet reception?
  Before DMA, VMM cannot know which VM is the destination of a received packet
    Unavoidable overhead with SW methods
    Two approches in Xen
Domain0
DomainU
Buffer
Packet
Page flipping (remapping)
- Zero-copy
Domain0
DomainU
Buffer
Packet
Page copying
- Single-copy
Packet
+ No copy cost
- Map/unmap cost
+ No map/unmap cost
(some costs before optimization)
- Copy cost
Network optimizations for PV guests [Xen Summit’06]

## Slide 8: Para-virtualization
Does copy cost outweigh map/unmap cost?
  Map/unmap involves several hypervisor interventions
    Copy cost is slightly higher than map/unmap (i.e., flip) cost
    “Pre-mapped” optimization makes page copying better than page flipping
      Pre-mapping socket buffer reduces map/unmap overheads
Network optimizations for PV guests [Xen Summit’06]
Page copying is the default in Xen

## Slide 9: Why HW Support?
Why not directly assign one NIC per VM?
  NIC is cheap HW
  Technically possible
    Selectively exposing PCI devices
    Giving I/O privilege to guest VMs
    Xen isolated driver domain (IDD)
  But, unreliable and insecure I/O virtualization
    Vulnerable to DMA attack
      DMA is carried out with machine addresses
      One VM can access another VM’s machine memory via DMA
      How to prevent?
        Monitoring every DMA request by using memory protection to DMA descriptor regions  Overhead!
Guest VM
Guest VM
Guest VM
VMM
Poor scalability: Slot limitation

## Slide 10: HW Support: IOMMU
I/O Memory Management Unit (IOMMU)
  Presenting a virtual address space to an I/O device
    IOMMU for direct I/O access of a VM: Per-VM address space
Level 2
Page
table
Page
table
Page
table
Page
table
Level 1
Page
table
. . .
Physical memory
Virtual address
MMU
Level 2
Page
table
Page
table
Page
table
Page
table
Level 1
Page
table
Virtual address
IOMMU
  Intel VT-d
  AMD IOMMU
  ARM SMMU
Secure direct I/O device access

## Slide 11: How to Deal with HW Scalability
How to directly assign NICs to tens of hundreds of VMs consolidated in a physical machine?
  PCI slots are limited
  Can a single NIC support multiple VMs separately?
    A specialized device for virtualized environments
      Multi-queue NIC
      CDNA
      SR-IOV

## Slide 12: HW Support: Multi-queue NIC
Multi-queue NIC
  A NIC has multiple queues
    Each queue is mapped to a VM
  L2 classifier in HW
    Reducing receive-side overheads
  Drawback
    L2 SW switch is still need
  e.g., Intel VT-c VMDq
Enhance KVM for Intel® Virtualization
Technology for Connectivity [KVMForum’08]

## Slide 13: HW Support: CDNA
CDNA: Concurrent Direct Network Access
  Rice Univ.’s project
  Research prototype: FPGA-based NIC
    SW-based DMA protection without IOMMU
Concurrent Direct Network Access in Virtual Machine Monitors [HPCA’07]

## Slide 14: HW Support: SR-IOV
SR-IOV (Single Rooted I/O Virtualization)
  PCI-SIG standard
  HW NIC virtualization
    Virtual function is accessed as
    an independent NIC by a VM
    No VMM intervention in I/O path
Source: http://www.maximumpc.com/article/maximum_it/intel_launches_industrys_first_10gbaset_server_adapter
  Intel 82599 10Gb NIC
Enhance KVM for Intel® Virtualization
Technology for Connectivity [KVMForum’08]

## Slide 15: Network Optimization Research
Architectural optimization
  Diagnosing Performance Overheads in the Xen Virtual Machine Environment [VEE’05]
  Optimizing Network Virtualization in Xen [USENIX’06]
I/O virtualization optimization
  Bridging the Gap between Software and Hardware Techniques for I/O Virtualization [USENIX’08]
  Achieving 10 Gb/s using Safe and Transparent Network Interface Virtualization [VEE’09]

## Slide 16: Inter-VM Communication
Analogous to inter-process communication (IPC)
  Split driver model has unnecessary path for inter-VM communication
    Dom1  Dom0 (bridge)  Dom2
H/W
Dom1
Dom2
Dom0
VMM
eth0
eth0
eth0
vif1.0
vif2.0
Bridge
Xen network architecture

## Slide 17: Inter-VM Communication
High-performance inter-VM communication based on shared memory
Research projects
  Depending on which layer is interposed for inter-VM communication
    XenSocket [Middleware’07]
    XWAY [VEE’08]
    XenLoop [HPDC’08]
    Fido [USENIX’09]

## Slide 18: Inter-VM Communication: XWAY
XWAY
  Socket-level inter-VM communication
    Inter-domain socket communications supporting high performance and full binary compatibility on Xen [VEE’08]
Interface based on
shared memory

## Slide 19: Inter-VM Communication: XenLoop
XenLoop
  Driver-level inter-VM communication
    XenLoop: a transparent high performance inter-vm network loopback [HPDC’08]
Module-based
implementation
 Practical

## Slide 20: Summary
I/O virtualization
  Focused on reducing performance overheads
    Network virtualization overhead matters in 10Gbps network
  Prevalent paravirtualized I/O
    Module-based split driver model has been adopted in mainline
  HW support for I/O virtualization
    SR-IOV NIC & IOMMU mostly eliminates I/O virtualization overheads

## Slide 21: GPU Virtualization

## Slide 22: GPU is I/O device or Computing unit?
Traditional graphics devices
  GPU as an I/O device (output device)
    Framebuffer abstraction
      Exposing screen area as a memory region
    2D/3D graphics acceleration
      Offloading complex rendering operations from CPU to GPU
        Library: OpenGL, Direct3D
      Why offloading?
        Graphics operations are massively parallel in a SIMD manner
        GPU is a massively parallel device with hundreds of cores
Why not a computing device?
  General-purpose GPU (GPGPU)
    Not only handling graphics operations, but also processing general parallel programs
    Library: OpenCL, CUDA

## Slide 23: GPU Virtualization
SW-level approach
  GPU multiplexing
    A GPU is shared by multiple VMs
    Two approaches
      Low-level abstraction: Virtual GPU (device emulation)
      High-level abstraction: API remoting
HW-level approach
  Direct assignment
    GPU pass-through
    Supported by high-end GPUs
GPU Virtualization on VMware’s Hosted I/O Architecture [OSR’09]

## Slide 24: SW-Level GPU Virtualization
Virtual GPU vs. API Remoting
 | Virtual GPU | API remoting
Method | Virtualzation at GPU device level | Virtualiztion at API level (e.g., OpenGL, DirectX)
Pros | Library-independent | VMM-independent GPU-independent
Cons | VMM-dependent GPU-dependent  Most GPUs are closed and rapidly evolving, so virtualization is difficult | Library-dependent But, a few libraries (e.g., OpenGL, Direct3D) are prevalently used (# of libraries < # of GPUs)
Use case | Base emulation-based virtualization (e.g., Cirrus, VESA) | Guest extensions used by most VMMs (Xen, KVM, VMware)

## Slide 25: API Remoting: VMGL
OpenGL apps in X11 systems
VMGL: VMM-Independent Graphics Acceleration [XenSummit’07, VEE07]

## Slide 26: API Remoting: VMGL
VMGL apps in an X11 guest VM
VMGL: VMM-Independent Graphics Acceleration [XenSummit’07, VEE07]

## Slide 27: API Remoting: VMGL
VMGL on KVM
  API remoting is VMM-independent
  WireGL protocol provides efficient 3D remote rendering
Guest VM
Guest OS
Host OS
(Linux)
KVM (kernel module)
QEMU
VirtIO-Net
Backend
VirtIO-Net
Frontend
Quake3
VMGL
Library
X Server
VMGL stub
Viewer

## Slide 28: HW-Level GPU Virtualization
GPU pass-through
  Direct assignment of GPU to a VM
  Supported by high-end GPUs
  Two types (defined by VMware)
    Fixed pass-through 1:1
      High-performance, but low scalability
    Mediated pass-through 1:N
GPU Virtualization on VMware’s Hosted I/O Architecture [OSR’09]
GPU provides multiple context,
so a set of contexts can be directly assigned to
each VM

## Slide 29: Remote Desktop Access: Industry
Remote desktop access technologies for high UX
  Citrix HDX
  Microsoft RemoteFX
  Teradici PCoIP (PC-over-IP)
VDI solutions
  VMware View with PCoIP
    VMware ESXi + PCoIP
  Citrix XenDesktop
    Xen + HDX + RemoteFX
  Microsoft VDI with RemoteFX
    Hyper-V + RemoteFX
  VirtualBridges VERDE VDI
    KVM + SPICE

## Slide 30: Remote Desktop Access: Open Source
SPICE
  Remote interaction protocol for VDI
    Optimized for virtual desktop experiences
    Actively developed by Redhat
    Based on KVM

## Slide 31: Remote Desktop Access: Open Source
SPICE (cont’)
Separate display thread per VM
(display rendering parallelization)
A VM (KVM) =
I/O thread (QEMU main)
+ Display thread
+ VCPU0 thread
+ VCPU1 thread
…

## Slide 32: Summary
GPU virtualization
  GPU is mostly closed
    Low-level GPU virtualization is technically complicated
    Instead, high-level abstraction well hides underlying complexity
      API remoting is an appropriate solution
  GPU is not only for client devices, but also for servers
    Virtual desktop infrastructure (VDI)
    GPU instance provided by public clouds
      Cluster GPU Instances for Amazon EC2